- Disassembling Top cover

Step 1:  Please remove 4 screws marked in red on the rear panel.

Step 2:  Please remove 4 feet pads by turning them counter clock wise.

Step 3:  Please remove the 4 feet pad mounting stations and remove the bottom cover plate.

Step 4:  Please remove the 12 screws circle in red.

Step 5: Once the screws are removed, pull the bottom part of the unit gently backward to reveal the gap in order to remove the cables circle in red.  Once the cables are detached, top cover can be gently removed.

- Disassembling copper cover and PSU cover

Step 1:  Please remove the 2 screws marked in red on the bottom of the unit.

Step 2:  Please remove the 6 screws marked in red in order to remove the copper cover and PSU cover.

Inner Top view of the unit

- Disassembling HPS-500 Switching power supply

Step 1:  Please remove the 3 screws marked in red and 4 cables marked in yellow.

Step 2:  Flip the unit and remove the 2 screws marked in red in order to remove the PSU.

- Disassembling capacitor board.

Step 1:  Please remove the cable marked in yellow and 4 screws marked in red in order to remove the capacitor board.

- Disassembling AMP board

Step 1:  Please de-soldering the wires (red and white) marked in yellow.

Step 2:  Please de-soldering the wires marked in yellow.

Step 3:  Please remove the cable marked in yellow and the screws and hex pillars marked in red in order to remove the AMP board.

- Disassembling MUTE Board

Please remove the 4 cables marked in yellow and 4 screws marked in red in order to remove the Mute board.

Index

- AMP Board (Ref-20 V3)

- Capacitor board

- MUTE board

- HPS-500 Switching power supply board